## Slide 1
Fortifying Industrial Control Systems: A Deep Dive into Evaluating Cryptographic Implementations
OCTOBER 21-24, 2024 | ATLANTA
By Nick Miles

## Slide 2
Cryptography
“A security system is only as strong as its weakest link.”
- Cryptography Engineering
2024 SecurityWeek ICS Cybersecurity Conference

## Slide 3
Cryptography Basics
  Block / Stream Ciphers
  Hashing Algorithms
  Digital Signatures / PKI
  Key Exchange
  TLS
Case Studies
Best Practices and Conclusions
  Passwords and Keys
  2FA
Agenda

## Slide 4
Ciphers
Plaintext
Cipher
Ciphertext
Plaintext
Ciphertext
Cipher
Block Cipher
Stream Cipher
one byte
one block
xor
keystream
Block Ciphers
AES (Rijndael)
  Block Size: 128 bit
  Key Sizes: 128, 192, 256 bits
3DES
  Block Size: 64 bit
  Key Sizes: 112 or 168 bits
Stream Ciphers
ChaCha20
  State Size: 512 bit
  Key Sizes: 128, 256 bits
RC4
  State Size: 2064 bits
  Key Sizes: 40-2048 bits

## Slide 5
Side Channel Attacks
ChipWhisperer – https://www.newae.com

## Slide 6
CMOS Data Bus
11111111 -> 00000000
11111110 -> 11111111
Hamming Weight Swings
Power Consumption
(8)
(1)

## Slide 7
AES
https://en.wikipedia.org/wiki/Rijndael_S-box

## Slide 8
Input Byte (first byte, first block) | Key Guess | AddRoundKey | SubBytes | Hamming Weight | Power Trace
0xF1 | 0x00 | 0xF1 | 0xA1 | 3 | 
0x13 | 0x00 | 0x13 | 0x7D | 6 | 
0xE2 | 0x00 | 0xE2 | 0x98 | 3 | 
0x83 | 0x00 | 0x83 | 0xEC | 5 | 
… | … | … | … | … | …
Correlation Power Analysis Attack

## Slide 9
Correlation Power Analysis Attack
Triggers (ChipWhisperer Husky)

## Slide 10
x
x
x
x
x
y
y
y
y
y

## Slide 12
Input Byte (first byte, first block) | Key Guess | AddRoundKey | SubBytes | Hamming Weight | Power Trace
0xF1 | 0x00 | 0xF1 | 0xA1 | 3 | 
0x13 | 0x00 | 0x13 | 0x7D | 6 | 
0xE2 | 0x00 | 0xE2 | 0x98 | 3 | 
0x83 | 0x00 | 0x83 | 0xEC | 5 | 
… | … | … | … | … | …
Correlation Power Analysis Attack
Total times running pearsonr: 255*16*[number of data points in trace]

## Slide 13
Applicability and Mitigation
TVLA (Test Vector Leakage Assessment)
PP-0084 (Secure IC)
  JHAS (Joint Hardware Attack Subgroup)
  JIL (score < 31 points, no attack path)
ISO 19790
  FIPS 140-3
ISO 17825
ISO/SAE 21434

## Slide 15
Other AES Issues
AES Modes
Oracle Attacks

## Slide 16
AES Modes

## Slide 17
Plaintext

## Slide 18
AES-ECB

## Slide 19
AES-CBC
Try yourself: https://github.com/int3grate/security_week_ics_2024/

## Slide 20
Oracle Attacks
Oracle primitive – hotter/colder
In practice:
  Error messages
  Response times
  Response length
Types:
  Compression
  Padding

## Slide 21
Compression Oracle Attacks
encrypt( compress( unknown_plaintext + attacker_choosen_text )) = ciphertext
Oracle: length( ciphertext )
Real world examples:
  CRIME – SPDY, HTTPS, TLS
  BREACH – HTTP compression over HTTPS
HTTP2 – hpack (special compression protocol to mitigate oracle attacks)
Mitigation: Don’t compress plaintext containing sensitive data

## Slide 22
Vulnerable Function:
Try yourself: https://github.com/int3grate/security_week_ics_2024/
Compression Oracle Attacks

## Slide 23
Padding Oracle Attack
0x66 | 0x6C | 0x61 | 0x67 | 0x7B | 0x50 | 0x4B | 0x43 | 0x53 | 0x37 | 0x5F | 0x46 | 0x54 | 0x57 | 0x7D | 0x01
0x66 | 0x6C | 0x61 | 0x67 | 0x7B | 0x50 | 0x4B | 0x43 | 0x53 | 0x37 | 0x5F | 0x46 | 0x54 | 0x03 | 0x03 | 0x03
0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10 | 0x10
0x66 | 0x6C | 0x61 | 0x67 | 0x7B | 0x50 | 0x4B | 0x43 | 0x53 | 0x37 | 0x5F | 0x46 | 0x54 | 0x57 | 0x02 | 0x02
One byte padding
Two byte padding
Three byte padding
Block appended if no padding
PKCS#7

## Slide 24
Padding Oracle Attack
XOR Properties
A ^ B = C
C ^ A = B
C ^ B = A

## Slide 25
Padding Oracle Attack – Homework
Prevention: Include and use MAC or HMAC to verify encrypted message integrity before performing any decryption.
Try yourself: https://github.com/int3grate/security_week_ics_2024/
Vulnerable Function:

## Slide 26
Cryptographic Hash Functions
Hashing Algorithms
  MD5 (deprecated)
  SHA1 (deprecated)
  SHA2 (256, 512), truncated 224/384
  SHA3
Input
Cryptographic Hash Function
Digest
“Hello World”
SHA256
a591a6d40bf420404a011733cfb7b190d62c65bf0bcda32b57b277d9ad9f146e
Avalanche Effect (from Wikipedia):

## Slide 27
Cryptographic Hash Function Properties
Pre-image
  Given a hash digest (the output of the hash function), it should be computationally infeasible to find any input message that produces that same digest.
Collision resistance
  It should be computationally difficult to find two messages that produce the same digest.

## Slide 28
Message Authentication Code (MAC)
m
m’
m
a = H(K,m)
m, a
m, a
m
Alice
Alice
Bob
Bob
Hacky McHackface
Hacky McHackface
A
B

## Slide 29
MAC Attacks
Replay Attacks
Mitigations (in message):
  Nonce
  Timestamps
  Sequence Number
Length Extension Attack
m = m1 + m2 + … + mk
m’ = m1 + … + mk + mk+1
h(m’) = h’(h(m), h(mk+1)
Note: m’ needs to include padding and length field.

## Slide 30
Length Extension Attack - PoC
Secret: my_secret_key (13 bytes)
Data: ?action=VIEW_PLC_STATUS

## Slide 31
Length Extension Attack - PoC

## Slide 32
Length Extension Attack - PoC
Try yourself:
https://github.com/int3grate/security_week_ics_2024/

## Slide 33
HMAC
HMAC – RFC 2104 (aka “Hash it again” approach)
K = key, text = plaintext, H = hash function
Protects against length extension, and potential key recovery attacks.

## Slide 34
CMAC – RFC 4493

## Slide 35
AES-GCM
P
AES-GCM
P
AD
T
C
AES-GCM
C
AD
T
Authenticated encryption with associated data (AEAD)
Encrypt
Decrypt
P – Plaintext
AD – Associated Data
C – Ciphertext
T – Tag or MAC

## Slide 36
Asymmetric Encryption
RSA, DSA, ECDSA
  Used for signing certificates, creating “chain of trust” used in PKI

## Slide 37
Key Exchange
DH (Diffie-Hellman)
DHE or ECDHE
  Ephemeral
Perfect Forward Secrecy (PFS / FS)

## Slide 38
TLS 1.3 is latest version. As of April 2024, 1.1 and 1.2 are deprecated.
If using TLS 1.3, you can be sure that it won’t use any of the insecure mechanisms listed on previous slides.
TLS 1.3 uses a shorter handshake than previous TLS versions, making it faster than previous versions.
TLS 1.3 only uses ephemeral keys exchanged using Diffie Hellman. You can’t add a key to Wireshark to decrypt this traffic, but there are other was to reverse engineer protocols using TLS 1.3.
Use TLS!!!

## Slide 39
Case Studies – Reverse Engineering Tools
Wireshark
Ghidra, IDA Pro
dnSpy (for .NET applications)
WinDBG
Tools:

## Slide 40
Identifying TLS – s7plus

## Slide 41
https://blog.viettelcybersecurity.com/security-wall-of-s7commplus-part-1/
Siemens DIY Crypto

## Slide 42
The average amount of information contained in message
Entropy Calculations

## Slide 43
StartTLS

## Slide 44
TLS Handshake (s7plus opportunistic / starttls TLS example)
Client Hello
Server Hello
Change Cipher Spec – 0x14 (for backwards compatibility)
0x17 – TLS Application Data

## Slide 45
TLS Headers
Type: 0x16
Version: (TLS 1.0)
Length: 0x00ea (234)

## Slide 46
S7plus TLS – v17 and up

## Slide 47
Reverse Engineering Protocols with TLS 1.3 – s7plus
My WinDBG Cheat Sheet:
https://github.com/int3grate/security_week_ics_2024/

## Slide 48
Reverse Engineering s7plus

## Slide 49
WinDBG Output

## Slide 50
Deprecated Algorithms
NIST has deprecated DES and 3DES. Use AES instead.
Remember: SHA1 and MD5 are deprecated also, used SHA256/512. RSA < 2048 is also deprecated.
Avoid hardcoded keys if possible.

## Slide 51
Password Storage (Client Side)

## Slide 52
Password Storage (Server Side)
Don’t store passwords, store their salted and hashed digests (using a cryptographically sound RNG source, and FIPS compliant hash algorithm).
  Salted SHA256 password hash: rnd_str + ‘$’ + SHA256(rnd_str+password)
Better yet, use an algorithm designed for storing passwords that is FIPS compliant.
  Argon2id
  scrypt
  bcrypt
https://cheatsheetseries.owasp.org/cheatsheets/Password_Storage_Cheat_Sheet.html

## Slide 53
Hardcoded Keys
https://medium.com/tenable-techblog/inside-simplisafe-alarm-system-291a8c3e4d89

## Slide 54
Improper Password Authentication
https://medium.com/tenable-techblog/examining-crypto-and-bypassing-authentication-in-schneider-electric-plcs-m340-m580-f37cf9f3ff34

## Slide 55
Authentication Bypass
HTTP Digest Auth
Server
Client
Salt, Challenge Value
Encrypted Challenge Value (using salted hash as shared secret)
Salted Hash
Password
CHAP (rfc1994)

## Slide 56
Conclusion
Use a popular, well supported cryptographic library in your projects rather than writing your own cryptographic functions. If possible, leave it as a shared library.
TLS 1.3 with certificate authentication is a complete solution for integrity, authentication, and confidentiality.
Don’t use deprecated cryptographic functions.
Encoding / obfuscation is not adequate for password protection.
Use HMAC rather than MAC.
Don’t assume hard coded encryption keys in hardware can’t be recovered.
Don’t use default passwords, and store them properly using salted hashes.
Don’t re-invent the wheel, look for prior work, and RFCs when designing new security mechanisms.
Have experts review you cryptographic implementations.

## Slide 57
Password Authentication Best Practices – End Users
Ideally random user IDs to prevent attackers guessing.
Use different authentication solution for remote access than what is used internally (LDAP, AD, etc…). Ideally something designed for this purpose that uses 2FA.
Passwords should be at least 8 characters. OWASP recommends using a password “strength” meter rather than complexity requirements which can result in more predictable passwords.
  https://github.com/zxcvbn-ts/zxcvbn
https://cheatsheetseries.owasp.org/cheatsheets/Authentication_Cheat_Sheet.html

## Slide 58
https://medium.com/@nmiles_19125
https://www.linkedin.com/in/nicholas-miles-7a6b1b34
nmiles@tenable.com
Questions?